| Product Specification |
| --- |
| Client： |  |
| Part No： | RZFT7060-6W2838(SP6W) |
| Product： | LED Module With Lens |
| Feature： | 6 pieces 2835 SMD LED. DC12V.175°lens.ABS Base |
| Client approval | Factory Approval | Audit | Account |
| RightLEDS CO.,LTD Address: 8-12F Complex building Mingjinhai Shiyan Town,Bao'anDistrict ,Shenzhen |

1.Features：

Good Heat Sink system. Low Brightness Decline. Span Life Up to 50,000hours Finest 2835 LED Package supplier in China to Guarantee High Efficacy ABS Base and Overall Lens Innovative Over-molded Way. Generate Finest China LED Module Double Faced Tape or Screw Hole to Make Installation Easier True 175 viewing angle True IP65

2.Application：over 10cm depth lighting box

3.Specification：

Photoelectric parameters Part No LED color Color temperature Voltage ( V ) Watt( W ) Lumen ( LM ) Efficiency (LM/W) View ( °) SP6W SMD2835 Day light 3000k, 6500k,7500k9000k 12 6 540 90 175 Cool white Physical parameters Series connection （PCS） Cover material Driver Weight（g） 20pcs Span life (Years) Size (mm) Working environment （℃） IP 20 ABS 12V(cv) 1080 67.5*60* 10.8 -25-+40 IP65 Note：① Test Condition Ta=25±2℃；②CV- constant voltage/CC-constant current ③ The mentioned data are typical. The real data are different from typical data.

4.Light Diagram and Light Distribution：

Light Distribution                            Light Diagram

5.Dimension（Unit/mm）：

6. Density Guide

| LED | Lighting box Depth1*(mm) | Density (pcs) | Min~Max (Lux) | Min~Max (cd/m2) |
| --- | --- | --- | --- | --- |
| SP6W | 100 | 9 | 2200-2600 | 810-962 |

7. Connection Layout

8.Installation：

Clean & remove all debris from the inside of the lighting box before you begin Remove tape backing and stick LED modules into place. Potting glass glue on both side of led module or screwing is recommended as security. Use screws, or silicone to secure at least every fifth LED module within the channel letter. Connect different lines of led module together. (1)Connect LED strips using in-line connectors or twist-on wire connectors (2)cut from middle of led modules. Peel off 10mm cover from wire. Connect the red wire (+) of the LED to the red wire (+) of another led strip. Connect the white wire (-) of the LED strip to white wire (-) of the another led strip. Insulate the connections. Test wire connections by hand. It is qualified if you can not pull off by hand. Test wire connections by turn on power supply. Must cap all exposed wires with appropriate wire connectors The connections between led strips and power supply should be covered by silicone or glass glue to prevent from water and rot The Max series connection should ne not over 20 when power supply run only from one side All electrical connections should be made within the Signage. Operate under turn off power Quality of power supply are strongly recommended to make sure the signage lighting last longer 9.Packing：

- 400pcs/carton    Carton Size：500*315*350mm

- Net Weight：19.0（1±10％）kg；Gross Weight：20（1±10％）kg；

- The quantity and weight can be different if packing be changed

【Note】

1.Handle them with care

2.Can not be operated in in inflammable and explosive place

3 .Operation should be under Turn off power

4. Can not be operated in place near heat source

5.Remove cover should be authorized

6.Any questions about led module. Please feel email us to get professional advice